## Slide 1
B.TECH AI · FINAL EVIDENCE REVIEW
Autonomous Parking System
Reinforcement Learning, Fuzzy Logic and a Safety Shield: what the evidence supports
Strict in-bay metric, retrained PPO, hybrid diagnosis and shield verification, all on held-out seeds
I069 Jia Jadhav
I072 Armaan Shaikh
B.Tech Artificial Intelligence
forward path
target bay
Recorded simulator episode, seed 9170 (a held-out far start picked to contrast outcomes): Fuzzy-precise ends fully inside the bay.
Notes: The drawing is a real recorded trajectory (viewer/assets/data/fuzzy_precise_seed9170.json). Seed 9170 was selected to contrast pose and strict outcomes, so it is illustrative, not typical.

## Slide 2
Headline: what changed and what did not
Pooled over 500 held-out episodes (seeds 3000-3099, 5000-5199, 9000-9199)
1.0 % → 57.8 %
Strict in-bay success, Fuzzy-only → Fuzzy-precise
The old 88 % was pose tolerance, not parked inside the lines.
5.8 % → 68.2 %
Pose success, original PPO → retrained PPO v2
Much better, but still below Fuzzy and it fails far starts (11 %).
0 collisions
With the braking-envelope shield, every controller
Costs completion: success drops, timeouts rise, some runs deadlock.
No RL benefit
RL + Fuzzy hybrid equals Fuzzy-only
A stall latch hands control to pure Fuzzy; PPO is not consulted.
Verdict: READY WITH CAVEATS. Strict success is bounded at about 58 %, no learned controller beats Fuzzy, and safety is shown only under the simulator’s own model.
Source: autonomous-parking/experiments/corrected_evaluation/summary_all.md; experiments/hybrid_diagnosis/; experiments/shield_verification/
Notes: Every number is from the corrected evaluation matrix. McNemar tests are paired on identical seeds.

## Slide 3
End-to-end workflow, as implemented
Each box maps to a file in the repository
Training
rl/train_ppo.py
PPO, curriculum,
validation seeds
Scenario +
Simulator
environment/
bicycle model, 8 rays,
OBB collision
Controller
selection
make_adapter()
fuzzy / PPO / hybrid
Safety shield
(optional)
integration/
envelope_shield.py
Evaluation
evaluation/
strict + pose metric,
McNemar, CIs
Visualisation
viewer/ (three.js)
replay of recorded
episodes
Observation (14): slot offset (world frame), heading error sin/cos, speed, steer angle, 8 ray distances. Action (2): steer, throttle/brake (negative = brake; forward-only, no reverse gear).
Inference path: observation → controller proposes action → (optional) envelope shield simulates one step then full braking; if the car footprint would hit anything, it replaces the action with hold-steer + full brake → simulator step.
The viewer replays recorded episodes. It is not live inference.
Notes: The shield is a model-based filter, not a learned component.

## Slide 4
Implemented now vs future work
Only the left column is claimed
IMPLEMENTED AND TESTED (131 tests pass)
Perpendicular parking simulator with randomised start pose and distance
Fuzzy-only and Fuzzy-precise navigators
PPO original (100k) and PPO v2 (retrained, ~420k)
Weighted RL + Fuzzy hybrid with fuzzy shield and stall latch
Braking-envelope shield, fail-closed on NaN
Strict in-bay metric next to legacy pose metric
Paired evaluation: exact McNemar, Wilson CIs, stratified by start distance
Replay viewer with strict-vs-pose HUD
FUTURE WORK (not claimed)
Reverse gear and re-manoeuvring (remaining strict misses are heading-limited)
Parallel parking results (code exists, excluded from every number)
Learned hybrid arbitration instead of hand-set weights
PPO that handles far starts (v2: 11 % on starts ≥ 4.5 m)
Shield that proposes its own escape action (today it only brakes)
Sensor noise, latency, moving obstacles, brake mismatch
Formal verification of the shield
Live in-browser inference in the viewer

## Slide 5
Corrected success metric: pose is not "inside the bay"
Same trajectories, two definitions. The geometry was not loosened.
bay 2.4 × 4.8 m
car 1.8 × 4.2 m, centred 0.32 m short of the slot centre (legacy stop radius)
only 0.30 m clearance at each end and 0.30 m each side
A heading error of 9° already swings a corner out: half-width = 0.9 cosθ + 2.1 sinθ = 1.22 m > 1.20 m
Pose success (legacy)
Centre ≤ 0.40 m from slot centre, heading error < 15°, speed ≤ 0.20 m/s for 2 steps, no collision. Looser than the 0.30 m bay clearance, so a "success" can overhang.
Strict (contained) success
Pose criterion AND the whole 4.2 × 1.8 m car footprint inside the bay lines (success_mode="contained"). Fuzzy-only drops from 88 % to 1 %; a smaller stop radius (0.10 m, tuned on seeds 7000-7099 only) lifts Fuzzy-precise to 58 %. Misses left are heading-limited: forward-only motion cannot re-manoeuvre.
Source: environment/parking_env.py; evaluation/tune_precision.py; tests/test_containment_metric.py

## Slide 6
Pose success vs strict success, n = 500
Failures retained; shared seeds across controllers
Chart: 
| Fuzzy-only (legacy) | Fuzzy-precise | PPO original | PPO v2 | RL + Fuzzy (orig.)
Pose success % | 88.2 | 88.2 | 5.8 | 68.2 | 87
Strict (in-bay) success % | 1 | 57.8 | 1.8 | 46.4 | 1
Paired tests (exact McNemar, pooled)
Fuzzy-precise vs PPO v2
strict success: 94 vs 37 discordant, p ≈ 7e-7
Fuzzy-only vs Fuzzy-precise
strict success: 0 vs 284, p ≈ 6e-86
Fuzzy-precise vs PPO v2
pose success: 106 vs 6, p ≈ 1e-24
Collision rates (pose mode): 11.8 / 11.8 / 43.4 / 4.2 / 13.0 %
Source: autonomous-parking/experiments/corrected_evaluation/summary_all.csv, paired tests in summary_all.md
Notes: Sets A (3000-3099), B (5000-5199) and C (fresh 9000-9199) pooled, n = 500. Note: the original PPO checkpoint used seeds 5000-5039 for best-checkpoint selection (overlap with set B); set C is clean.

## Slide 7
Same start, three controllers: recorded trajectories (seed 9170)
Authentic episodes from the simulator, drawn from the viewer’s recorded JSON
Fuzzy-only (legacy)
Stopped within pose tolerance, NOT inside the bay
Fuzzy-precise
Parked inside the bay (0.21 m, 5.7°)
PPO v2
Parked inside the bay (0.09 m, 0.1°)
Seed 9170 is a held-out far start chosen because it contrasts the outcomes; it is not a typical episode. On far starts PPO v2 usually fails (see the PPO slide).
Notes: Cyan outline = start pose, coloured outline = final pose. Heights and widths of the car outlines use the real 4.2 x 1.8 m footprint, scaled with the map.

## Slide 8
PPO: original was under-trained; v2 is better but still limited
Retrained with the curriculum recipe, 3 seeds, ~420k steps each; selected on validation seeds 7000-7099
Chart: Pose success % by start distance (n = 181 / 170 / 149)
| Near (<2.5 m) | Mid (2.5-4.5 m) | Far (≥4.5 m)
Fuzzy-only | 96.7 | 88.8 | 77.2
PPO v2 | 97.8 | 86.5 | 11.4
PPO original | 6.1 | 7.1 | 4
Candidates (validation)
six checkpoints: 55-70 % success, 2-6 % collision
Selected: seed 3 best, 70 % / 3 %
Pooled held-out
pose 68.2 %, strict 46.4 %, collision 4.2 %
Original: pose 5.8 %, collision 43.4 %
Training notes
reward normalisation is configured but never used; no observation normalisation
Reading: PPO v2 matches Fuzzy near the bay and collapses on far starts. We claim "much better than the original", not "better than Fuzzy".
Source: autonomous-parking/models/README.md; autonomous-parking/experiments/corrected_evaluation/stratified.md; experiments/ppo_retrain/

## Slide 9
Why RL + Fuzzy equals Fuzzy-only: the stall latch
Measured on 100 seeds of the original hybrid; PPO is queried and its output is state-dependent
1 Spawn
Mamdani shield fires in ~77 % of episodes (about 45 % of starts are within 0.3 m of a neighbour)
2 Brake
Shield brakes, car stays still, PPO action is overridden
3 Latch
After 12 stalled steps (1.2 s) control goes to pure FuzzyOnlyController
4 Fuzzy drives
PPO and shield are no longer consulted; latch fires in 96 of 100 episodes
Chart: PPO v2 + Fuzzy, no latch: outcome % by RL weight (seeds 8000-8099)
| 0 | 0.25 | 0.5 | 0.75
Success | 80 | 77 | 76 | 70
Collision | 20 | 23 | 11 | 5
Timeout | 0 | 0 | 13 | 25
Without the latch the original hybrid gets 3 % success and 97 % timeouts.
No RL weight raised success; more RL weight traded collisions for timeouts.
Pooled 500 episodes: hybrid pose success 87.0 % vs Fuzzy-only 88.2 % (McNemar 7 vs 1, p = 0.07).
Source: experiments/hybrid_diagnosis/; tests/test_hybrid_integrity.py

## Slide 10
Envelope shield: collisions go to zero, completion pays for it
Pose-mode outcomes, n = 500, without and with the shield
Chart: No shield
| Fuzzy-only | PPO original | PPO v2 | RL + Fuzzy
Success | 88.2 | 5.8 | 68.2 | 87
Collision | 11.8 | 43.4 | 4.2 | 13
Timeout | 0 | 50.8 | 27.6 | 0
Chart: With envelope shield
| Fuzzy-only | PPO original | PPO v2 | RL + Fuzzy
Success | 83.8 | 5.8 | 66.6 | 83.4
Collision | 0 | 0 | 0 | 0
Timeout | 16.2 | 94.2 | 33.4 | 16.6
Deadlock, not caution: 60 of 81 Fuzzy-only+shield timeouts never moved more than 1 m. The shield rejects every proposed action and proposes none of its own (active in 96 % of steps, median final distance to the slot 4.27 m).
Collision-free only under its own model: with real brakes at 0.85× the modelled strength, 49 of 198 adversarial episodes collide (0.7×: 114, 0.5×: 156).
Source: experiments/shield_verification/*.json; evaluation/shield_stress.py

## Slide 11
Seed 3009: collision without the shield, a freeze with it
Recorded trajectories (left) and frames from the rendered 3D viewer (right)
Fuzzy-only: collision after 22 steps
Fuzzy-only + shield: brakes, times out
Viewer frames captured in headless Chromium with software WebGL. Camera framing in top-down and chase modes was not verified.

## Slide 12
Scenario validity and known limits
Absolute rates depend on the start generator; the ranking evidence is paired
44.6 % of starts
have body clearance < 0.30 m to a neighbour (6.4 % < 0.05 m); start distance is uniform in [0.05, 1] × 6 m, so many starts begin beside the bay.
Forward-only
The car cannot re-manoeuvre; remaining strict misses are heading-limited. Reverse code exists but is excluded from every number.
Model-based safety
Ground-truth geometry, perfect brakes, no latency, no moving obstacles. Not formally verified.
Selection overlap
The original PPO checkpoint’s best-model selection used seeds 5000-5039 (overlaps set B). Fresh set C (9000-9199) is clean for every controller.
Illustrative seeds
Seed 9170 in the viewer was picked to contrast outcomes. One simulator, perpendicular parking only.
Small hand-set parts
Hybrid weights and shield thresholds are hand-set; stop radius tuned on seeds 7000-7099 only.
Source: autonomous-parking/experiments/corrected_evaluation/start_features.csv, stratified.md; models/README.md

## Slide 13
What we claim, and what we do not
Verdict: READY WITH CAVEATS
SAFE TO CLAIM
Fuzzy-precise parks fully inside the bay in 57.8 % of 500 held-out episodes
The legacy 88 % is pose tolerance, strict is 1 %
Retrained PPO v2 is far better than the original PPO
The hybrid equals Fuzzy-only because of the stall latch
The shield gave 0 collisions in every simulated run, at the cost of completion
DO NOT CLAIM
"RL + Fuzzy beats Fuzzy-only" (it does not)
"PPO solves parking" (it fails far starts)
"Collision-free" without "in this simulator model"
"Formally verified" or "universally safe" shield
"Parks inside the bay" for the legacy Fuzzy-only
That 9170 is a typical episode

## Slide 14
Reproduce and inspect
Python 3.11+ required (pinned dependency versions)
cd autonomous-parking
python -m pytest tests/ -q # 131 passed
python -m evaluation.evaluate_matrix # resumable
python -m evaluation.summarize_corrected
python -m evaluation.stratify
python -m evaluation.shield_stress
python prepare_comparison.py --seed 9170
python ../viewer/serve.py # replay viewer
python demo.py --controller fuzzy_precise+env --seed 3009
Evidence
README.md
CHANGELOG.md
PRESENTATION_READINESS_AUDIT.md
PROFESSOR_DEFENSE_QA.md
DEMO_RUNBOOK.md
autonomous-parking/experiments/
corrected_evaluation/
hybrid_diagnosis/
ppo_retrain/
shield_verification/